## Slide 1: CCUS in SINOPEC
LUN Zengmin, CUI Maolei, ZHOU Bing
Notes: the developing of EOR technique in SINOPEC, on behalf of the research group, especially Professor Lun and Dr. Cui
PEPRIS: Petroleum exploration and production research institute of SINOPEC

## Slide 2: Brief introduction on SINOPEC
SINOPEC Group is the largest integrated national energy and petrochemical company in China.
E&P
Refinery
Sale
Petrochemical
  The 2rd largest oil & gas producer in China
  The 2rd largest refinery in the world
  The 4th largest ethylene producer in the world

## Slide 3: Brief introduction on PEPRIS
Petroleum Exploration and Production Research Institute is a secondary unit of SINOPEC Group. Its business mainly includes the development of technology, supporting the E&P of oil field, strategy research, etc.
Oil&Gas Planning Office
Strategy Research Office
Oil&Gas Exploration Office
Geophysical Research Office
Unconventional Resource Office
Enhance Oil Recovery Office
…

## Slide 4: Contents
China’s CCUS Policies and Actions
1.
SINOPEC CCUS Strategy
2.
SINOPEC CCUS Projects
3.
SINOPEC CCUS Technology
4.

## Slide 5: China’s CCUS Policies and Actions
中国能源结构变化趋势(国家统计局)
China stands firm on reducing CO2 emissions. At the Paris Climate Conference in December 2015, President Xi pledged to reduce carbon dioxide emissions per unit of GDP will be lowered by 60~65% per by 2030, compared with 2005.

## Slide 6
Governmental Policies: Since 1990s, a series of CCUS policies and regulations were formulated to promote the development of CCUS technology
China’s CCUS Policies and Actions

## Slide 7
Governmental Policies: Provincial governments responded positively & actively
16 Provinces and cities have issued policies to promote the development of CCUS;
20 CCUS related regulations & policies were published by local governments of :
Beijing (2), Shanghai (3), Shaanxi (2), Ningxia (2), and Henan (1), Hubei(1), Jiangsu(1), Anhui(1), Zhejiang(1), Hunan(1), Jilin(1), Jiangxi(1), Guangdong(1), Heilongjiang(1), Chongqing(1)
China’s CCUS Policies and Actions

## Slide 8
Pilot & demonstration projects: The Ministry of Science and Technology has funded a series of national R&D programs to carry out systematic theoretical study and applied technology research, and to promote the application of CCUS.
Fundamental research
National funding
Technology prototype and Pilot test
973 Project
Applied technology
863 Project
Industrial Application
Industrial support
973 Project
863 Project
National Special fund
CCUS Development
University
Research
Institute
Industry
China’s CCUS Policies and Actions

## Slide 9
Support from Oil & Gas Industry: A strategic alliance of CCUS industry technology innovation was established by enterprises, schools and colleges in order to promote the innovation and development of CCUS technology and industry in China.
China’s CCUS Policies and Actions

## Slide 10
Support from Oil & Gas Industry: Chinese companies are actively promoting the development and application of CCUS technology, and carried out more than 20 CCS pilot projects.
CO2 Capture | Shengli Power Plant Flue gas Capturing, SINOPEC
 | Tail Gas capture from Zhongyuan Chemical Plant, SINOPEC
 | Recovery of High carbon Natural Gas from Songnan Gas Field, SINOPEC
CO2 EOR | CO2 flooding Project of Shengli Oilfield, SINOPEC
 | CO2 flooding Project of Zhongyuan Oilfield, SINOPEC
 | CO2 flooding Project of Caoshe Oilfield, SINOPEC
 | CO2 flooding Project of Yaoyingtai Oilfield, SINOPEC
 | Jilin oilfield CO2-EOR, CNPC
 | Daqing oilfield CO2-EOR, SINOPEC
 | Yanchang oilfield CO2-EOR, Yanchang Petroleum
CCUS | CO2 utilization in Chemical Engineering, Zhongkejinlong
 | Beijing thermal power plant CO2 Capture, Huaneng group
 | degradable plastics, CNOOC
 | Shidongkou CO2 Capture, Huaneng group
 | Shuanghuai Power Plant CO2 Capture, State Power Investment
 | Clean Coal Energy Power system
 | Coal Oil and CCUS, Shenghua Group
 | Microalgae carbon sequestration and bioenergy project, ENN Group
 | Green Coal Power IGCC Power Plant CCUS Demostration Project, Huaneng Group
 | 35MWt Oxygen-enriched Combustion Technology, Huazhong University of Science and Technology
SINOPEC
CNPC
China’s CCUS Policies and Actions

## Slide 11
Asia Development Banl,2015
China MOST, 2018
China CCUS Roadmap:
2015-2030: to acquire the ability of CCUS industrialization and verify the feasibility of new technology;
2030-2040: to achieve CCUS industry cluster and to conduct commercial CCUS project;
2040-2050: to realize the extensive deployment of CCUS
China’s CCUS Policies and Actions

## Slide 12: Contents
China’s CCUS Policies and Actions
1.
SINOPEC CCUS Strategy
2.
SINOPEC CCUS Projects
3.
SINOPEC CCUS Technology
4.

## Slide 13: SINOPEC low-carbon strategy
Green and low-carbon strategy, as one of the core strategies, enables SINOPEC to develop rapidly and sustainably.
Resource strategy
Integration strategy
Low carbon strategy
Internationalization strategy
Market strategy
Differentiation strategy
Global Fortune 500 Tops

## Slide 14: SINOEPC low-carbon activities
In 2018, Sinopec has launched a Green Enterprise Action Plan. Green and low-carbon activities promote the progress to be the resource-saving and environment-friendly enterprise
Green enterprise action plan
2018
2011
2013
2014
2016
2017
Green & low carbon strategy
To be one of the core strategies
Blue sky & Clear water action
870 projects and 20.92 billion RMB
Energy efficiency multiplier program
1930 projects, saving coal 3.37 million tonnes
Shale gas achievement
Fuling shale gas field with the productivity of 10 billion m3, and the proved reserves of 600.8 billion m3
Xiongan mode for geotherm
Heat supply: 5╳107 m2
substitutable coal: 1.42 million tonnes,
CO2 mitigation: 3.70 million tonnes

## Slide 15: SINOEPC CCUS strategy
long-range perspective
2030-2050
Short term
Present-2020
Diversification
Scalization
Commercialization
Industrial application for CO2 EOR and storage
Larger scale demonstration project for CO2 utilization and storage
Prior development to CO2 EOR and storage
Technical reserves for CO2 utilization and storage
CO2 source and sink match planning
long-medium term
2020-2030
Technical capacity building
Industrial capacity building
Industrial application

## Slide 16: Contents
China’s CCUS Policies and Actions
1.
SINOPEC CCUS Strategy
2.
SINOPEC CCUS Projects
3.
SINOPEC CCUS Technology
4.

## Slide 17: SINOPEC CCUS R&D Projects
CCUS R&D projects have been conducted since 1990s, which accumulate abundant experience.
1990 2000 2010 2015年 2020
Caoshe
Gao 89
Yaoyingtai
Pucheng
Zhangjiaduo
Shengli Power plant
Songnan natural
gas proceesing
Zhongyuan
Petrochemical plant
Shengli Power Plant
Qilu Petrochemical
Zhenglizhuang Oilfield
Mineralization
Microalgae oil
Xianhe Oilfield
Zhongyuan
Petrochemical plant(II)
Gao 899
EGR
EWR
Utilization
EOR
Capture
Difficulty
Fuming
Chujialou

## Slide 18: Pucheng Case (Zhongyuan Oilfield)
Source: Zhongyuan Petrochemical plant
Capture method: MEA
CO2 source: 16.6%
Capture capacity: 20,000 t/a
Accumulative injection amount： 550 thousands tons
Reservoir type: Water-flooded abandoned reservoir, Pucheng oilfield
Permeability: 696 ╳10-3µm2
Temperature: 85℃
Water cut: 98%
Injection Scenario: CO2 WAG miscible
Well: 22 injectors and 38 producers
Incremental RF: 9.9%

## Slide 19: Yaoyingtai Case (Dongbei oilfield)
Source: Songnan natural gas processing
Capture method: MDEA
CO2 source: 23%
Capture capacity: 500,000 t/a
Accumulative injection amount: 289 thousand tons
Reservoir type: low permeability high water cut reservoir, Yaoyingtai oilfield
Permeability: 1.9 ╳10-3µm2
Temperature: 97.5℃
Injection Scenario: CO2 immiscible
Well: 39 producers and 12 injectors
Incremental RF: 6.27%

## Slide 20: Gao 89 Block Case (Shengli Oilfield)
Source: Shengli Power Plant
Capture method: MSA
CO2 source: 14%
Capture capacity: 40,000 t/a
Accumulative injection amount: 269.9 thousands tons
Reservoir type: low permeability reservoir, Gao 89 block, Shengli oilfield
Permeability: 4.7 ╳10-3µm2
Temperature: 97.5℃
Injection Scenario: CO2 near-miscible
Well: 15 producers and 11 injectors
Incremental RF: 12.7%

## Slide 21: Caoshe Case (Huadong Oilfield)
2005-7
2006-10
2006-2
2005-7
2007-6
0
20
40
60
80
100
2001年10月
2002年10月
2003年10月
2004年10月
2005年10月
2006年10月
2007年10月
2008年10月
2009年10月
2010年10月
2011年10月
2012年10月
2013年10月
新井注气增油(t/d)
新井投产产油（t/d)
老井CO2增油(t/d)
压裂+深抽增产(t/d)
无措施递减预测(t/d)
waterflooding
Side injection
Fracturing
& deepening
CO2-EOR from new wells
CO2-EOR from old wells
Source: Natural CO2 gas produced from Subei basin
Accumulative injection amount: 196 thousand tons
Reservoir type: Taizhou formation, Caoshe Oilfield, Subei Basin
Permeability: 24.77╳10-3µm2
Temperature: 110℃
Formation Pressure: 32MPa
Injection Scenario: CO2 miscible
Well: 15 producers and 5 injectors
Incremental RF: 7.89%

## Slide 22: CO2 EOR and storage Cases
Reservoir type: high water cut, low permeability, tight.
Project Number: 26
Incremental injection amount: 1.77×106 tons
Incremental oil recovery: 28×104 tons
Oil exchange rate: 0.16 t/t CO2.
Tahe Oilfield
Baolang oilfield
Dongbei
Honghe oilfield (Huabei)
Shengli Oilfield
Zhongyuan oilfield
Jiangsu oilfield
Huadong oilfield

## Slide 23: CCS-EOR industrial bases
Two large scale projects
--Shengli Power Plant: 1.0 million t/a
--Qilu Refinery plant: 0.6 million t/a
Three industrial bases
--Shengli Oilfield
--Zhongyuan Oilfield
--Subei basin (Huadong & Jiangsu)
Shengli Power Plant
(project appraisal)
CO2 EOR Pilot Tests
Qilu petrochemical coal gas(partial implementation
FANG48-CNPC
HONGHE-SINOPEC
GAO 89-SINOPEC
PUCHENG-SINOEPC
CHUJIANGLOU-SINOPEC
CAOSHE-SINOPEC
)
CO2 PILOT TESTS
HEI59-CNPC
YAOYINGTAI-SINOPEC
FUMING-SINOPEC
SHU101-CNPC
HONG87-CNPC

## Slide 24: Contents
China’s CCUS Policies and Actions
1.
SINOPEC CCUS Strategy
2.
SINOPEC CCUS Projects
3.
SINOPEC CCUS Technology
4.

## Slide 25: Full-chain CCS-EOR technologies
Capture
transport
EOR & storage
Recycle & utilization

## Slide 26: CO2 Capture Technology
New capture solvents have been developed to tackle the issues of corrosion, higher energy consumption, amine loss.
Carbon Capture Solvent
Solvent absorption
Ionic liquid method
Solid adsorption
Low temperature distillation
Membrane separation
Notes: the absorption mechanism of polyamino weak base
the antioxidant degradation mechanism of reaction chain blocking
Polyamino capture solvent:
high efficiency
low energy consumption
anti degradation
low corrosion
Capture process
absorption heat pump + MVR
reduce the energy consumption
reduce the circulating water consumption

## Slide 27: CO2 Capture Technology
Self-developed product of MSA-II solvent has a more superior performance than the normal MEA.
Absorption capacity (L/L)
Corrosion rate (mm/a)
Oxidation degradation rate(%)
Increase by 30%
Decrease by 97%
Decrease by 98%
Notes: 中国石化在二氧化碳捕集与利用领域具有50多年的研发历史，

## Slide 28: CO2 Transportation
Three CO2 transportation ways have been successfully tested in CO2 EOR pilot tests.
CO2 Pipeline in Shengli oilfield
--20km, gas phase transport
CO2 Truck in Zhongyuan oilfield
--low temp., liquid phase transport
CO2 ship in Huadong oilfield
--low temp., liquid phase transport
Shengli oilfield--pipeline
Huadong oilfield--ship
Zhongyuan Oilfield--truck

## Slide 29: CO2 EOR and Storage Technology
CO2 EOR Laboratory
PVT
Capillary viscometer
Multipoint Long core holder
Phase behavior
Multiphase flow
Interfacial tension and diffusion
Miscibility and Micro-visualization
Micro-physical simulation system
Slim-tube device
Interfacial tension
Foam flooding system
Diffusion coefficient
Interfacial tension device

## Slide 30: CO2 EOR and Storage Technology
Numerical simulation integrated CO2 EOR and storage
CO2 partition coefficient
Hysteresis effect
CO2 mineralization
2
1
3
EOR
Storage
Injection time
Oil rate
ω1 =0.9
ω2 =0.1
ω1 =0.5
ω2 =0.5
ω1 =0.1
ω2 =0.9
initial stage: EOR
Mid-term: EOR and storage
later stage: storage
CO2 storage mechanisms in EOR
Full life circle of CO2 EOR and storage
Optimizing parameter

## Slide 31: CO2 EOR and Storage Technology
Chemical enhancement CO2 EOR technologies
CO2 MMP Reducer
CO2 emulsifier
CO2 foam
CO2 particle
CO2 gel
CO2 thickener
CO2-chemical enhancement system
MMP reduction agent
Mobility control agents
—ethers regulator
—oil soluble surfactant (Isobutyl citrate)
—Supercritical CO2 soluble surfactant with auxiliaries
—CO2 thicker
—CO2 emulsifier
—CO2 foam agent
—CO2 particle gel
—CO2 gels
stepping control to improve sweep efficiency
Notes: Low P
Heterogeneity
Poor quality

## Slide 32: CO2 EOR and Storage Technology
Multiphase flow simulation in wellbore
anti-corrosive chemical agent
coupon corrosion test
Injection-production and anti-corrosion technology
wellhead
Critical point
(bubble point)
formation
Multiphase flow
Single phase flow

## Slide 33: CO2 EOR and Storage Technology
CO2 recycle and reinjection technology
CO2 purity > 96%
Moisture < 200ppm
Low energy consumption: 150kw.h/tCO2
Membrane separation with simple operation and low investment
diagram map of rectification with low temperature stripping
Features:

## Slide 34
CO2 monitoring and safety evaluation
CO2 EOR and Storage Technology

## Slide 35: CO2-EOR of tight sandstone reservoir
Prospects for EOR
By now, CO2 is one of the best way to enhance recovery in China.
China has over 10 billion tons resource in tight reservoirs, which are suitable for CO2 EOR.
Yanchang formation in Ordos
The Permian in Jungle
middle-lower Jurassic
Shahejie formation in Bohai Bay
Qingshan Formation in Songliao

## Slide 36: CO2-EOR of tight sandstone reservoir
Overview of target formation：
Wellsite map of GroupⅠin Jinnan formation
Jinnan oil field lies in the North Jiangsu Basin
4 staged fractured horizontal wells were drilled in two tight oil areas
CO2 injection was implemented in 2014.

## Slide 37: CO2-EOR of tight sandstone reservoir
CO2-EOR displacement mechanism
PVT visualized device of HPHT
Bubble point
Bubble point increased, oil viscosity decreased, oil swelling
Be benefit for oil recovery as the increasing of CO2 injection volume.
Immiscible displacement
Bubble point Pressure— CO2 injection
CO2 mole, %
CO2 mole, %
Oil viscosity— CO2 injection
Oil volume factor— CO2 injection
CO2 mole, %
Bubble point pressure, MPa
Oil viscosity, mPa·s
Oil volume factor
Oil recovery
CO2 injection pressure, MPa

## Slide 38: CO2-EOR of tight sandstone reservoir
CO2-EOR mechanism
CO2 diffusion and extraction effect (NMR)
The fractures in matrix provide large contact area between oil and CO2, playing an important role in CO2 diffusion and extraction effect to enhance oil recovery.
Pore diameter,

## Slide 39: CO2-EOR of tight sandstone reservoir
CO2-EOR mode
Coupled huff and puff with well patterns
The fractures in matrix provide large contact area between oil and CO2, playing an important role in CO2 diffusion and extraction effect to enhance oil recovery.
Physical simulation
Numerical simulation

## Slide 40: CO2-EOR of tight oil reservoir
pilot test
Obvious effect of EOR
Total injection of CO2：4406 tons
Increased oil production： 4692 tons
Oil/CO2：1.06 ton/ton
EOR：4.7%.

## Slide 41: CO2 EWR and storage technology
Case study on Ordos basin shows a big potential for CO2 EWR and storage.

## Slide 42: CO2 EGR and storage technology
Pre injection 2h 20h 42h
CO2-CH4 diffusion process (25MPa, 85℃)
Incremental RF: 17.3%
CO2 EGR mechanisms indicate the technical feasibility to integrate EGR and storage
Injection pore volume
Recovery factor,%
CO2 concentration,%
Time, h
Storage front
displacement front
Natural gas zone
SCCO2+Natural gas zone
SCCO2 Storage zone
Gas injection front
Gas injection trail edge

## Slide 43: CO2 chemical utilization technology
Bio-refinery and CO2 utilization
-Biomass+CO2 succinic acid, butanediol, et.
-Every 1kg succinic acid generates, 0.37kg CO2 can be sequestrated.
-Succinic acid, butanediol can be utilized to produce biological engineering plastics.
Research on CO2/CH4 dry reforming
-Primary reaction：CO2+CH4——2CO+2H2
-Secondary reaction：H2+CO2——CO+H2O

## Slide 44: CO2 mineralization utilization technology
A series of techniques on CO2 mineralization have been proposed, including solid waste phosphogypsum, tail gas CO2 mineralization phosphogypsum.
SINOPEC is cooperating with Sichuan University.

## Slide 45: CO2 biology utilization technology
CO2 microalgae oil
In 2009, the study on microalgae oil was launched. In 2010, microalgae cultivation laboratory was established, and some researches on microalgae-cultivation-oil were carried out .
Demonstration unit in refinery
CO2 emissions demonstration unit in Shijiazhuang refinery with 500m3 of microalgae was completed, and put into trail operation.

## Slide 46: CONCLUSIONS
CCUS has been an indispensable part of green-low carbon strategy to promote the sustainable development for SINOPEC.
SINOPEC has implemented many demonstration projects in diversification and full chain, including capture, transportation, EOR, utilization and storage.
SINOPEC has the technical competence to promote the development of CCUS in China.

## Slide 47: Thanks for your attention!
LUN Zengmin
Lunzm.syky@sinopec.com
CUI Maolei
Cuiml.syky@sinopec.com
ZHOU Bing
Zhoubing.syky@sinopec.com